## Slide 1: Environmental cleaning and disinfection
Dr Lata Kapoor
Joint Director National Centre for Disease Control Govt. of India

## Slide 2: Outline
Environmental cleaning and Disinfection
  Environmental decontamination
  Cleaning of medical equipment
  Cleaning soiled bedding, towels and clothes from patients with COVID-19
  Cleaning and disinfection of occupied patient rooms
  Cleaning and disinfection after patient discharge and transfer
  Prevent environment contamination: contain respiratory secretions

## Slide 3: Environmental Decontamination (1)
General Principles
Healthcare environment contains a diverse population of microorganisms, but only few are significant pathogens
Microbiologically contaminated surfaces can serve as reservoirs of potential pathogens
Contaminated surfaces not directly associated with transmission of infections to either staff or patients
Transfer of microorganisms from environmental surfaces to patients is mostly via hand contact with the surface
Hand hygiene is important to minimize the impact of this transfer
Cleaning and disinfecting environmental surfaces is fundamental in reducing healthcare-associated infections
Notes: Microbiologically contaminated surfaces can serve as reservoirs of potential pathogens – these surfaces generally are not directly associated with transmission of infections to either staff or patients
Transfer of microorganisms from environmental surfaces to patients is mostly via hand contact with the surface

## Slide 4: Environmental Decontamination (2)
COVID-19 virus can potentially survive in the environment for several hours/days
Premises and areas potentially contaminated with the virus to be cleaned before their re-use
Products containing antimicrobial agents known to be effective against coronaviruses may be used
Established cleaning strategies to be used
  Remove the majority of bioburden
  Disinfect equipment and environmental surfaces

## Slide 5: Environmental Decontamination (3)
Housekeeping surfaces can be divided into two groups
  Those with minimal hand contact (e.g. floors and ceilings)
  “High touch surfaces” – those with frequent hand-contact
High touch housekeeping surfaces in patient-care areas should be cleaned and/or disinfected more frequently
  Doorknobs
  Bedrails
  Light switches
  Wall areas around the toilet in the patient’s room
  Edges of privacy curtains

## Slide 6: Cleaning and disinfection of medical equipment (1)
Wear gloves when handling/transporting used patient care equipment
Before removing equipment from patients room, medical equipment must be disinfected
Non-critical medical equipment
  Usually only require cleansing followed by low- to intermediate-level disinfection, depending on the nature and degree of contamination
  E.g. stethoscopes, blood pressure cuffs, dialysis machines and equipment knobs and controls

## Slide 7: Cleaning and disinfection of medical equipment (2)
In absence of manufacturer instructions regarding cleaning/disinfection of equipment
  Ethyl alcohol or isopropyl alcohol (70%, v/v) often used to disinfect small surfaces (rubber stoppers of multiple-dose medication vials, and thermometers) and occasionally external surfaces of equipment (stethoscopes and ventilators)
Alcohol causes discoloration, swelling, hardening and cracking of rubber and certain plastics after prolonged and repeated use

## Slide 8: Cleaning and disinfection of medical equipment (3)
Difficult to clean surfaces and equipment
Barrier protection of difficult to clean surfaces and equipment is useful, especially if these surfaces are
  Touched frequently by gloved hands during the delivery of patient care
  Likely to become contaminated with body substances
Impervious-backed paper, plastic or fluid-resistant covers are suitable for use as barrier protection (cover mattresses for easier disinfection)
Remove and discard/disinfect coverings with gloved hands
Perform hand hygiene after ungloving
Cover these surfaces with clean materials before the next patient encounter

## Slide 9: Cleaning and disinfection of medical equipment (4)
Area/Items | Inputs | Process | Method/ procedure
Stethoscope | Alcohol-based rub/Spirit swab | Cleaning | Should be cleaned with detergent and water regularly Should be wiped with alcohol based rub/spirit swab before each patient contact
BP cuffs & covers | Detergent Hot water | Washing | Cuffs should be wiped with alcohol- based disinfectant and regular laundering is recommended for the cover
Thermometer | Detergent and water Alcohol rub Individual thermometer holder | Cleaning | Should be stored dry in individual holder, inverted Clean with detergent and tepid water and wipe with alcohol rub in between patient use Preferably one thermometer for each patient
Injection and dressing trolley | Detergent and water Duster Disinfectant (70% alcohol) | Cleaning | To be cleaned daily with detergent and water After each use should be wiped with disinfectant

## Slide 10: Cleaning soiled bedding, towels and clothes from patients with COVID-19 (1)
Clean laundry and surfaces in all environments in which COVID-19 cases receive care – at least once a day and when a patient is discharged
Hospital disinfectants:
  70% alcohol for small areas – reusable dedicated equipment (e.g. thermometers)
  Sodium hypochlorite at 1% for surface disinfection
Staff dealing with soiled bedding, towels and clothes from patients with COVID-19 should:
  Wear appropriate PPE – heavy duty gloves, mask, eye protection (goggles/face shield), long-sleeved gown, apron (if gown is not fluid resistant), and boots or closed shoes
  Never carry soiled linen against body; place soiled linen in a leak-proof bag or bucket
  Perform hand hygiene after blood/body fluid exposure and after PPE removal

## Slide 11: Cleaning soiled bedding, towels and clothes from patients with COVID-19 (2)
Soiled linen should be placed in clearly labelled, leak-proof bags or containers, carefully removing any solid excrement and putting in covered bucket to dispose of in the toilet
Washing machine
  Wash at 60-90°C with laundry detergent followed by soaking in 0.01% chlorine for approximately 30 minutes and dried
No machine washing
  Soaked in hot water with soap/detergent in a large drum
  Use a stick to stir and avoid splashing
  Empty the drum and soak linen in 0.01% chlorine for approx. 30 minutes
  Rinse with clean water and let linens dry fully in the sunlight

## Slide 12: Cleaning and disinfection of occupied patient rooms
Designate specific well-trained staff for cleaning environmental surfaces
Cleaning personnel should wear PPE and must be trained on proper use of PPE and hand hygiene
Define the scope of cleaning to be done each day
Use a checklist to promote accountability for cleaning responsibilities
Keep cleaning supplies outside the patient room

## Slide 13: Cleaning of Housekeeping surfaces and eating utensils
Housekeeping surfaces:
  Regularly clean and remove soil and dust
  Personal protective equipment (PPE) to be used during cleaning and housekeeping procedures
  Clean only with soap and water or a detergent/disinfectant, depending on the nature of the surface and the degree of contamination
Dishes and eating utensils used by a patient with known or suspected infection
  No special precautions other than standard precautions
  Wear gloves when handling patient trays, dishes and utensils

## Slide 14: Spill management
Worker assigned to clean the spill should wear gloves and other personal protective equipment
Most of the organic matter of the spill to be removed with absorbent material
Surface to be cleaned to remove residual organic matter
Use disinfectant: hypochlorite
  1% for small spills
  10% for large spills

## Slide 15: Cleaning and disinfection after patient discharge or transfer
Clean and disinfect all surfaces that were in contact with patient or may have become contaminated during patient care
Do not spray or fog occupied or unoccupied rooms with disinfectant – potentially dangerous practice that has no proven benefits

## Slide 16: Prevent environment contamination: contain respiratory secretions (1)
Ensure early recognition and prevention of transmission of the respiratory virus at the initial encounter with a healthcare setting
Practice respiratory hygiene/cough etiquette
Ensure availability of materials for adhering to respiratory hygiene/cough etiquette in waiting areas for patients and visitors
Masking and separation of persons with symptoms of respiratory infection/Universal masking

## Slide 17: Summary
Cleaning and disinfecting environmental surfaces is fundamental in reducing healthcare-associated infections
Established cleaning strategies to be used, rigorously monitored
Cleaning staff must be protected by use of standard precautions including use of appropriate PPE
Prevent environment contamination by containing respiratory secretions

## Slide 18: Thank you